## Slide 1: I Want My Voice to Be Heard: IP over Voice-over-IP for Unobservable Censorship Circumvention
Amir Houmansadr (The University of Texas at Austin)
Thomas Riedl (University of Illinois at Urbana-Champaign)
Nikita Borisov (University of Illinois at Urbana-Champaign)
Andrew Singer (University of Illinois at Urbana-Champaign)

## Slide 2: Internet Censorship
The Internet is a big threat to repressive regimes!
Repressive regimes censor the Internet:
  IP filtering, DNS hijacking, Deep packet-inspection, etc.
Circumvention systems

## Slide 3: New stage in the arms race
The threat model has changed
Past: detect circumvention end-points
Now: detect circumvention traffic also
We need traffic unobservability
against passive, active, or proactive analysis

## Slide 4: A recent approach
A promising approach: hide circumvention traffic within popular Internet protocols
  Censors are unlikely to completely block that protocol
A new trend: mimic the target protocol
  SkypeMorph, StegoTorus, and CensorSpoofer (CCS’12)
It’s hard to imitate network protocols
The Parrot is Dead: Observing Unobservable Network Communications [Oakland’13]
FLAWED

## Slide 5: Our approach
We seek the same objective, but take a different approach:
  Run the target protocol
By running the target protocol no need to worry about implementation quirks, bugs, protocol details
Challenge: how to efficiently encapsulate traffic into the target protocol

## Slide 6: FreeWave: IP over Voice-over-IP
Target protocol: Voice-over IP (VoIP)
Why VoIP
  Widely used protocol (only 663 Million Skype users)
    Collateral damage to block
  Encrypted
How to hide?
  The dial-up modems are back!

## Slide 7: FreeWave architecture
Client
FreeWave
Server

## Slide 8: System components

## Slide 9: MoDem component
A typical acoustic modem
  QAM modulation
Reliable transmission
  Turbo codes
  Use Preambles

## Slide 10: Evaluations

## Slide 11: FreeWave’s unobservability
Comprehensive unobservability at the protocol level
Traffic analysis (packet rates and sizes)
Fixed rate codecs (e.g., G.7 series)
  Not an issue 
Variable bit-rates (e.g., Skype’s SILK)
  Simple analysis
  Superimpose with recoded conversation

## Slide 12: Server obfuscation
Client
FreeWave
Server

## Slide 13: Future directions
Embed into Video of VoIP
Find other protocol to tunnel
  Look for better efficiency
IP over Voice-over-IP
Voice over
IP over
…

## Slide 14: Questions!